## Slide 1: Conversion Number System

## Slide 2: Decimal Number System
Decimal number system is a base 10 number system having 10 digits from 0 to 9. This means that any numerical quantity can be represented using these 10 digits. Decimal number system is also a positional value system.
  Example– 734, 971 and 207. The value of 7 in all three numbers is different−
    In 734, value of 7 is 7 hundreds or 700 or 7 × 100 or 7 × 102
    In 971, value of 7 is 7 tens or 70 or 7 × 10 or 7 × 101
    In 207, value 0f 7 is 7 units or 7 or 7 × 1 or 7 × 100

## Slide 3: Decimal Number System
734
10 is the Base Number.
0, 1 and 2 are the Exponents.
Hundreds | Tens | ones
7 | 3 | 4
10^2 | 10^1 | 10^0

## Slide 4: Binary Number System
The easiest way to vary instructions through electric signals is two-state system – on and off. On is represented as 1 and off as 0, though 0 is not actually no signal but signal at a lower voltage. The number system having just these two digits – 0 and 1 – is called binary number system.

## Slide 5: Binary Number System
Each binary digit is also called a bit.
The rightmost digit is called least significant bit (LSB) and leftmost digit is called most significant bit (MSB).

## Slide 6: Conversion of Decimal to Binary Numbers
The remainders are to be read from bottom to top to obtain the binary equivalent.
4310 = 1010112

## Slide 7: Conversion of Decimal to Binary Numbers

## Slide 8: Conversion of Negative Decimal to Binary Numbers
-10
  Binary 10 0 0 0 0 1 0 1 0
  1’s Complement 1 1 1 1 0 1 0 1 (change 1 to 0 and 0 to 1)
  2’s Complement 1 1 1 1 0 1 0 1 (add 1 to 1’s complement) + 1
                1 1 1 1 0 1 1 0